## Slide 1: NFPA 70E CHANGES AND OSHA 1910.269
By G. Tom Machacek
Cornerstone Electrical Consultants, Inc.

## Slide 2: NFPA 70E CHANGES AND OSHA 1910.269
Cornerstone Electrical Consultants, Inc. produced this presentaation as awareness information for the 2015 Beyond Safety Conference attendees. All other inquiries for permission to reproduce materials may be submitted by written request to the Board of Directors of Cornerstone Electrical Consultants, Inc.
Resource Acknowledgement:
NFPA 70E-2015 OSHA 1910 & 1926
IEEE Standard 1584-2004 CUTLER HAMMER
IEEE PCIC – SAFETY SEMINARS Bussman Fuses
Electrical Contractor Mag. Jan. 2014 ESFI
EHS Today Hugh Hoagland – E Hazard
DISCLAIMER
Cornerstone Electrical Consultants, Inc. does not and cannot know all the facts of your particular situation, and, as such, the information provided herein is not intended to create any express or implied warranty to the reader. The content of this manual is intended for informational purposes only, and the reader’s adoption and/or application of information provided herein is performed strictly at the reader’s own risk. Cornerstone Electrical Consultants, Inc.’s clients and friends should conduct an independent investigation of the facts for their particular situation and exercise their own judgment as to the appropriate solution based upon the results thereof.
Copyright © 2015 by Cornerstone Electrical Consultants, Inc.
All rights reserved.

## Slide 3: ARE YOU HERE TO LEARN ABOUT THIS BIG BANG THEORY?

## Slide 4: ARE YOU HERE TO LEARN ABOUT THIS BIG BANG THEORY?

## Slide 5: THE BIG BANG FROM AN ARC FLASH IS NO THEORY!
IT IS REAL!

## Slide 6: AND THE RESULTS ARE NEVER GOOD.

## Slide 7: THE CHOICES I MAKE DICTATE THE LIFE I LEAD.
Tim Autrey

## Slide 8: THE CHOICES I MAKE DICTATE THE LIFE I LEAD.
Tim Autrey
OUR BETTER CHOICES COME WITH A BETTER UNDERSTANDING OF THE RISKS AND CONSEQUENCES OF OUR CHOICES.
THIS IS WHY WE ARE HERE TODAY – TO PREVENT A BAD DAY!

## Slide 9: PRESENTATION OBJECTIVES
WHAT IS AN ELECTRICAL ARC FLASH/ BLAST?
WHAT ARE SOME OF THE NFPA 2015 CHANGES?
WHAT IS THE DIFFERENCE BETWEEN OSHA 1910.300 (Subpart S) AND 1910.269 (Subpart R)?
WHAT ARE SOME OF THE 269 CHANGES?

## Slide 10
ARC FLASHES DO HAPPEN!
The number of arc flash incidents in the United States is greater than many engineers realize since most accidents don't make the daily news. Chicago-based Capelli-Schellpfeffer, Inc. reports that five to ten arc-flash injuries that result in hospitalization occur every day.

## Slide 11
AN IMPORTANT MOTOR STOPS AND YOU ARE TOLD – “GET IT RUNNING NOW”!
Your choices?
Are you protected?
What if something happens?

## Slide 18
Notes: There is a new requirement in the 2002 National Electrical Code® for arc flash hazard labeling.

## Slide 19: WITHIN SECONDS, YOUR LIFE AND YOUR FAMILY’S HAS CHANGED!

## Slide 20
AN ARC FLASH IS AN UNPLANNED, UNCONTROLLED RELEASE OF ELECTRICAL ENERGY RESULTING IN:
INTENSE RADIANT HEAT
COPPER GASES
MOLTEN METAL
RAPID PRESSURE WAVE

## Slide 21
ELECTRICAL ARC
Pressure Waves
Copper Vapor:
Solid to Vapor
Expands by
67,000 times
Molten Metal
Intense Light
Hot Air–Rapid Expansion
35,000 °F
Shrapnel
Sound Waves

## Slide 22: HISTORY OF NFPA 70E
OSHA PROPOSED TO REPLACE THE REFERENCE TO THE 1971 NATIONAL ELECTRICAL CODE IN THE MANDATORY APPENDIX WITH NFPA 70E.

## Slide 23: NFPA 70E SECTIONS
ARTICLE 110 GENERAL REQUIREMENTS
  TRAINING
  1. The skills and techniques necessary to distinguish exposed electrical conductors or circuit parts from other parts of electrical equipment,
  2. The skills and techniques necessary to determine the nominal voltage of exposed energized electrical conductors or circuit parts,
  3. The approach distances specified in Table 130.4 (D) (a) and Table 130.4 (D) (b) and the corresponding voltages to which the qualified person will be exposed.

## Slide 24: NFPA 70E SECTIONS
ARTICLE 110 GENERAL REQUIREMENTS
  TRAINING
  4. The decision-making process necessary to be able to do the following:
  Perform the job safety planning
  Identify electrical hazards
  Assess the associated risk
  Select the appropriate risk control methods from the hierarchy of controls identified in 110.1(G), including personal protective equipment.

## Slide 25: NFPA 70E SECTIONS
ARTICLE 110 GENERAL REQUIREMENTS
  RESPONSIBILITY
  MULTIEMPLOYER RELATIONSHIP
Whenever outside servicing personnel are to be engaged in activities covered by the scope and application of this standard, the on-site employer and the outside employer(s) shall inform each other of existing hazards, PPE/clothing requirements, safe work practice procedures, and emergency / evacuation procedures applicable to the work to be performed. This coordination shall include a meeting and documentation.

## Slide 26: NFPA 70E SECTIONS
ARTICLE 130 –
WORK INVOLVING ELECTRICAL HAZARDS:
  Electrically safe working conditions
  Working while exposed to electrical hazards
  Approach Boundaries
  Arc Flash Risk Analysis
  Other precautions for personnel activities
  PPE and other protective equipment
  Underground electrical Lines and Equipment
  Cutting or Drilling

## Slide 27: NFPA 70E DEFINITIONS
  Qualified Person – One who has demonstrated skills and knowledge related to the construction and operation of electrical equipment and installations and has received safety training to identify and avoid the hazards involved.
  Unqualified Person – A person who is not a qualified person.
THE TITLE OF “ELECTRICIAN” DOES NOT MAKE ONE QUALIFIED. EACH INDIVIDUAL MUST BE ABLE TO DEMONSTRATE SKILL TO PERFORM THE TASK TO BE CLASSIFIED AS A QUALIFIED ELECTRICIAN.

## Slide 28: NFPA 70E DEFINITIONS
  Incident Energy –
  The amount of thermal energy impressed on a surface, a certain distance from the source, generated during an electrical arc event. Incident energy is typically expressed in calories per square centimeter (cal/cm2).
  Incident Energy Analysis –
  A component of an arc flash hazard risk assessment used to predict the incident energy of an arc flash for a special set of conditions.

## Slide 29: WHAT ARE MY WORKING BOUNDARIES?

## Slide 30
Limited Shock Boundary: Qualified or Unqualified Persons* * Only if accompanied by Qualified Person
Prohibited Shock Boundary: Qualified Persons Only. PPE as if direct contact with live part
Restricted Shock Boundary: Qualified Persons Only
Note: Shock boundaries dependent on system voltage level
Flash Protection Boundary (FPB)
Must wear appropriate PPE.
FPB dependent on fault level and time duration
Equipment

## Slide 31: AC APPROACH DISTANCES NFPA 70E Table 130.4(D)(a)

## Slide 32: DC APPROACH DISTANCES NFPA 70E Table 130.4(D)(b)

## Slide 33
Limited Shock Boundary: Qualified or Unqualified Persons* * Only if accompanied by Qualified Person
Prohibited Shock Boundary: Qualified Persons Only. PPE as if direct contact with live part
Restricted Shock Boundary: Qualified Persons Only
Note: Shock boundaries dependent on system voltage level
Flash Protection Boundary (FPB)
Must wear appropriate PPE.
FPB dependent on fault level and time duration
Equipment

## Slide 34
Human Tissue – Tolerance To
Second Degree Burn
0.00
0.50
1.00
1.50
2.00
2.50
0.01
0.1
1
3
5
7
9
Exposure Time, seconds
Incident Energy
Absorbed,
cal/cm
2
1.2 cal/cm2 Minimum
1.2

## Slide 35: SUN BURN TIMES

## Slide 36
Human Tissue – Tolerance To
Second Degree Burn
0.00
0.50
1.00
1.50
2.00
2.50
0.01
0.1
1
3
5
7
9
Exposure Time, seconds
Incident Energy
Absorbed,
cal/cm
2
1.2 cal/cm2 Minimum
1.2

## Slide 37
Table 130.7(C)(16) Protective Clothing and Personal Protective Equipment (PPE)
PPE Category 1:
Note: The PPE Category 0 was eliminated in the 2015 edition.

## Slide 38
Table 130.7(C)(16) Protective Clothing and Personal Protective Equipment (PPE)
PPE Category 2:

## Slide 39
Table 130.7(C)(16) Protective Clothing and Personal Protective Equipment (PPE)
PPE Category 3:

## Slide 40
Table 130.7(C)(16) Protective Clothing and Personal Protective Equipment (PPE)
PPE Category 4:

## Slide 41: WHAT SAFETY MEASURES CAN BE TAKEN TO LIMIT EXPOSURES TO LESS THAN 1.2 CAL/CM2?
LOCKOUT – DO NOT WORK ENERGIZED.
ONLY QUALIFIED AND NECESSARY PERSONNEL WITHIN THE FLASH PROTECTION BOUNDARY
INCREASE DISTANCE E~1/D2
CLOSE DOORS AND COVERS.
USE PROPER PPE CATEGORY FOR THE LEVEL OF ENERGY.

## Slide 42
From
EHS
Today

## Slide 43: BODY PPE
AR RAINWEAR

## Slide 44: HOW CAN I DETERMINE WHAT FLASH RISK CLASS CATEGORY I WILL ENCOUNTER?
LABELS ON SWITCHGEAR
TABLES FOR EQUIPMENT WITHOUT LABELS

## Slide 48: Table 130.7(C)(15)(A)(a) Arc-Flash Hazard Identification for AC & DC Systems

## Slide 49: Table 130.7(C)(15)(A)(a) Arc-Flash Hazard Identification for AC & DC Systems

## Slide 50: Table 130.7(C)(15)(A)(a) Arc-Flash Hazard Identification for AC & DC Systems

## Slide 51: Table 130.7(C)(15)(A)(a) Arc-Flash Hazard Identification for AC & DC Systems

## Slide 52: Table 130.7(C)(15)(A)(a) Arc-Flash Hazard Identification for AC & DC Systems

## Slide 53: Table 130.7(C)(15)(A)(a) Arc-Flash Hazard Identification for AC & DC Systems

## Slide 54: Table 130.7(C)(15)(A)(b) Arc-Flash Hazard PPE Categories for Alternating Current Systems

## Slide 55: Table 130.7(C)(15)(A)(b) Arc-Flash Hazard PPE Categories for Alternating Current Systems

## Slide 56: Table 130.7(C)(15)(B) Arc-Flash Hazard PPE Categories for Direct Current Systems

## Slide 57: Table 130.7(C)(15)(B) Arc-Flash Hazard PPE Categories for Direct Current Systems

## Slide 58: ENERGIZED WORK
Additional hazards or increased risk – Energized work shall be permitted where the employer can demonstrate that de-energizing introduces additional hazards or increased risk.
Infeasibility – Energized work shall be permitted where the employer can demonstrate that the task to be performed is infeasible in a de-energized state due to equipment design or operational limitations.

## Slide 59: ENERGIZED WORK, Cont.
Less than 50 Volts – Energized electrical conductors and circuit parts that operate at less than 50 volts shall not be required to be de-energized where the capacity of the source and any overcurrent protection between the energy source and thw worker are considered and it is determined that there will be no increased exposure to electrical burns or to exposure due to electric arcs.

## Slide 60: ENERGIZED WORK, Cont.
Normal Operation – Normal operation of electric equipment shall be permitted where all of the following conditions are satisfied:
  Equipment is properly installed,
  Equipment is properly maintained,
  Doors are closed and secured,
  All covers are in place and secured, and
  No evidence of impending failure.

## Slide 61: ENERGIZED ELECTRICAL WORK PERMIT WHEN REQUIRED
When energized work is permitted in accordance with 130.2(A), an energized electrical work permit shall be required under the following conditions:
When work is performed within the restricted approach boundary.
When the employee interacts with the equipment when conductors or circuit parts are not exposed but an increased likelihood of injury from an exposure to an arc flash hazard exists.

## Slide 62: EXEMPTIONS TO WORK PERMIT
An energized electrical work permit shall not be required if a qualified person is provided with and uses appropriate safe work practices and PPE in accordance with Chapter 1 under any of the following:
Testing, troubleshooting, and voltage measuring
Thermography and visual inspection if the restricted approach boundary is not crossed.

## Slide 63: EXEMPTIONS TO WORK PERMIT, Cont.
An energized electrical work permit shall not be required if a qualified person is provided with and uses appropriate safe work practices and PPE in accordance with Chapter 1 under any of the following:
Access to and egress from an area with energized electrical equipment if no electrical work is performed and the restricted boundary is not crossed
General housekeeping and miscellaneous non-electrical tasks if the restricted approach boundary is not crossed.

## Slide 64: SECTION 200 - MAINTENANCE
Single-lines up to date
Equipment maintained per manufacturer’s spec.
Protective devices maintained and tested
Clearances
Grounding and Bonding
Safety locks, interlocks, other controls
Identification and warning signs
Hazardous (Classified) locations
Batteries and rooms

## Slide 65: OSHA SUBPARTS S AND R
1910.300 Subpart S – General Electrical Installation and Utilization including industrial substations.
1910.269 Subpart R – Operation and Maintenance of electrical power generation, transmission, distribution.

## Slide 66: OSHA SUBPARTS S AND R
1910.269(a)(i) [0] Note:
The types of installations covered … include the generation, transmission, and distribution of electric utilities, as well as equivalent installations of industrial establishments. Subpart S of this part covers supplementary electrical generating equipment … to supply … emergency, standby, or similar purposes only.

## Slide 67: OSHA 1910.269

## Slide 68: OSHA 1910.269

## Slide 69: OSHA 1910.269

## Slide 70: OSHA 1910.269

## Slide 71: OSHA 1910.269

## Slide 72: OSHA 1910.269

## Slide 73: OSHA 1910.269

## Slide 74
GOOD DAY
OR
A BAD DAY?
YOUR CHOICE!